## Slide 1: Prediction of Solidification crack susceptibility of 7XXX series aluminium alloys using ML
21MMB0A24 Ishika Jaiswal
21MMB0A40 Mohit Tripathi
21MMB0A55 Ram Prasad
21MMB0A41 Sathwik Nandala

## Slide 2: contents
Introduction
    Solidification Cracking Mechanism
    Contributing Factors
    Mitigation Strategies
Problem Identification & Objectives
Literature Review
Methodologies
Result
Discussion
Conclusion

## Slide 3: 1.(A) Solidification Cracking Mechanism
Definition:
Cracks that form during the final stages of solidification, when the material transitions from liquid to solid.
Caused by the inability of the solidifying material to withstand tensile stresses.
Mechanism:
Formation of liquid films at grain boundaries.
Thermal contraction during cooling generates tensile stress.
Liquid films fail to accommodate the stress, leading to cracks.
Why to Study Solidification Cracking?
A key challenge in processing these alloys, particularly during welding or casting.
Impacts structural integrity, leading to failures in critical applications.
1. Introduction

## Slide 4: 1.(b) Factors Contributing to Solidification Cracking
Alloy Composition:
High zinc content increases solidification range, making the alloy more susceptible.
Impurities like iron and silicon promote cracking by segregating at grain boundaries.
Cooling Rate:
Faster cooling leads to finer grains, reducing cracking.
Solidification Range:
Wider range means more time spent in the brittle semi-solid state, increasing risk.
Grain Structure:
Columnar grains aligned in one direction exacerbate cracking; equiaxed grains reduce it. Fine grains improve cracking resistance.

## Slide 5: 1.(C) Mitigation Strategies
Alloy Design:
Adjust zinc, magnesium, and copper content to narrow the solidification range.
Reduce impurity levels to minimize grain boundary segregation.
Process Parameters:
Use controlled cooling rates to avoid steep thermal gradients.
Preheating and post-processing to relieve stresses.
Grain Refinement:
Add grain refiners like titanium or zirconium to encourage the formation of equiaxed grains.
Welding Techniques:
Utilize techniques like friction stir welding to minimize residual stresses.
Employ weld preheating and post-weld heat treatment.

## Slide 6: 2.(a) Problem identification
Solidification cracking is a critical defect occurring during solidification processes like casting, welding, and additive manufacturing.
Unavailability of data set for model building.
Existing methods to predict solidification cracking rely on experimental techniques, which are time-consuming and costly.
2. Problem identification
& Objectives

## Slide 7: 2.(b) objectives
Develop machine learning models to predict solidification cracking susceptibility (classification task).
To predict hardness (regression task) using alloy composition.
Enhance the understanding of factors influencing the properties through feature engineering.

## Slide 8: 3. Literature Survey( Related to ML)
Author / Journal | Title | Key findings
S Feng et al. / Materials Science and Engineering | Predicting solidification cracking susceptibility of stainless steels using machine learning | Machine learning models effectively predict solidification cracking susceptibility in stainless steels based on composition and processing parameters. Feature selection techniques identified key factors influencing cracking, improving predictive accuracy. The study demonstrated that ML-based predictions could aid in designing crack-resistant stainless steel alloys.
Dhilip A et al. / Materials and Manufacturing Processes | Machine learning predictive approaches for hot crack mitigation in modified TIG welded AA7075 joints | ML models were used to optimize TIG welding parameters to reduce hot cracking in AA7075 aluminum alloys. The study identified critical factors such as heat input and filler material selection that influence crack formation. Predictions made by ML models significantly improved weld quality, reducing defects in high-strength aluminum alloys.
Umer Masood Chaudry et at. / Materials Today Communications | Machine learning-aided design of aluminum alloys with high performance | ML techniques successfully predicted the hardness of aluminum alloys, optimizing compositions and aging conditions. The Gradient Boosted Tree model provided the highest accuracy in predicting alloy performance. The study demonstrated ML’s capability to accelerate the discovery of high-performance aluminum alloys, reducing reliance on traditional experimentation.

## Slide 9: 3. Literature Survey( Related to ML)
Author / Journal | Title | Key findings
Fan Zhang et al. / Metals | Prediction of Cracking Susceptibility of Commercial Aluminum Alloys during Solidification. | Machine learning models were used to predict solidification cracking in commercial aluminum alloys based on composition and cooling rates. The study identified key factors affecting crack formation, enabling improved alloy design to minimize defects. ML-based predictions provided a reliable alternative to traditional experimental methods, saving time and costs in alloy development.
Alireza Valizadeh et al. / Science and Technology of Advanced Materials | Alloys innovation through machine learning | ML techniques accelerated the discovery of novel alloys by predicting their mechanical properties based on composition and processing conditions. The study demonstrated that data-driven approaches improve efficiency in materials design, reducing reliance on trial-and-error experiments. ML-driven alloy innovation can significantly enhance performance across various applications, from aerospace to manufacturing.

## Slide 10: 3. Literature Survey ( Related to 7xxx Aluminium alloy)
Author / Journal | Title | Key findings
C. M. Cheng et al. / Science and Technology of Welding and Joining | Hot cracking of welds on heat treatable aluminium alloys. | Hot cracking in heat-treatable aluminum alloys is strongly influenced by weld solidification characteristics and alloy composition. Controlling solidification parameters and using appropriate filler materials can significantly reduce crack susceptibility. The study provided insights into mitigating hot cracking through optimized welding techniques and alloy modifications.
E. Lavernia et al. / Materials Science and Engineering, | Rapid Solidification Processing of 7XXX Aluminium Alloys: A Review. | Rapid solidification processing improves mechanical properties and reduces segregation in 7XXX aluminum alloys. This technique enhances the strength and corrosion resistance of the alloys, making them suitable for high-performance applications. The study highlighted advancements in rapid solidification methods and their impact on the microstructure and performance of 7XXX alloys
A.K.Mukhopadhyay et al. / Materials Science Forum | Key Microstructural Features Responsible for Improved Stress Corrosion Cracking Resistance and Weldability in 7xxx Series Al Alloys Containing Micro / Trace Alloying Additions | Micro/trace alloying elements improve stress corrosion cracking resistance and weldability in 7XXX aluminum alloys. These additions refine grain structure and reduce the formation of detrimental phases during welding and heat treatment. The study demonstrated how microstructural optimization enhances the performance and durability of 7XXX series alloys.

## Slide 11: 3. Literature Survey
Paper 1:
  Predicting solidification cracking susceptibility of stainless steels using machine learning.
Paper 2:
  Machine learning predictive approaches for hot crack mitigation in modified TIG welded AA7075 joints.
Paper 3:
  Machine learning-aided design of aluminum alloys with high performance.

## Slide 12
Paper 4:
  Hot cracking of welds on heat treatable aluminium alloys.
Paper 5:
  Alloys innovation through machine learning: a statistical literature review.
Paper 6:
  Prediction of Cracking Susceptibility of Commercial Aluminum Alloys during Solidification.

## Slide 13
Paper 7:
  Rapid Solidification Processing of 7XXX Aluminium Alloys: A Review.
Paper 8:
  Key Microstructural Features Responsible for Improved Stress Corrosion Cracking Resistance and Weldability in 7xxx Series Al Alloys Containing Micro / Trace Alloying Additions

## Slide 14: Progress of work
Data Collection
Data Source:
  Experimental data from literature review, and existing datasets.
  Dataset includes various samples of 7xxx aluminum alloys.
Key Features:
  Alloy Composition:
    Major elements: Zn, Mg, Cu.
    Minor elements: Si, Fe, Cr, Mn, Ti.
  Processing Parameters:
    Cooling rate, heat treatment conditions, grain size, strain rate.
  Target Variables:
    Crack susceptibility (classification: high, medium, low).
    Hardness

## Slide 15: work we’ll do
Data Preprocessing
Cleaning:
  Removal of outliers.
  Handling missing values using imputation techniques.
Normalization:
  Scaling features to a range of [0, 1].
Feature Engineering:
  Deriving new features like the Zn:Mg ratio and grain boundary misorientation.
  Principal Component Analysis (PCA) for dimensionality reduction.

## Slide 16: work we’ll do
Training Algorithms
Classification Models:
  Decision Tree.
  Random Forest.
  Support Vector Machine (SVM).
  Deep Neural Networks (DNN).
Regression Models:
  Linear Regression.
  XGBoost.
Cross-Validation:
  Split dataset into training (70%), validation (15%), and testing (15%).

## Slide 17: work we’ll do
Model Evaluation
Metrics for Classification:
  Accuracy, Precision, Recall, F1-Score.
Metrics for Regression:
  Mean Absolute Error (MAE), Root Mean Squared Error (RMSE), R² Score.
Hyperparameter Tuning:
  Grid search and Bayesian optimization.

## Slide 18: Result

## Slide 19: Discussion

## Slide 20: conclusion
  Machine learning effectively predicts cracking susceptibility and hardness.
  Identifies key factors influencing properties, guiding alloy design and process optimization.

## Slide 21: Future work
Expand dataset with experimental results.
Investigate other mechanical properties like toughness and fatigue resistance.
Development of advanced alloys with reduced susceptibility to cracking.
Exploration of innovative welding and casting techniques for improved structural integrity.

## Slide 22: Thank you